Student Instructions: Adopted from Pack 530

Reference: https://pack168.scoutingplanner.com/userdata/pack168/Building%20A%20P-530%20Rocket.pdf

Water Bottle Rocket

What is a Water Bottle Rocket?

A water bottle rocket is a 1 or 2-liter (soda) bottle with compressed air (for safety reasons we keep the

air pressure around 40 to 50psi) and water released in an upward direction.

A water bottle rocket is both a simple project and a fun one that any level Cub Scout can build with a

little help from a parent. Not only is it easy to build but it can also be used to teach Newton’s Laws of

motion, forces, energy and flight as well as the scientific method.

Once the rockets are built they can be launched at a den meeting or at a Pack outing. Our Pack has

an annual Fall Family Campout and we launch them there. Your rocket launching could include

events such as, long distance, hitting a target, landing an egg safely, or even making a field goal, but

if you want to keep is simple the boy can have a blast just launching the water bottle and watching is

go up.

Construction

Almost any 1 or 2 liter bottle will work; however, some bottles have a mouth or opening (nozzle) that

is too small to accommodate the launch tube. The launch tube is a regular 1/2 inch piece of PVC

tubing. The tube should slide snugly into the nozzle of the bottle forming a nearly air tight seal. We

have found that the majority of CokeTM related 2 liter bottles and Sam’s Choice 1 liter water bottle will

work while a majority of PepsiTM related bottles will not. This is not to say that the smaller nozzle

bottles are worthless, rather they should be used for other components of the rocket like the nose

cones.

#1 MAIN BODY/PRESSURE CHAMBER

The main part of your rocket is the body or PRESSURE CHAMBER. Peel the label off

your bottle and try to clean the glue residue the best that you can. Do NOT use a knife

or other object to scrape the label off.  Scrape marks can weaken the plastic.  Also, do

not use hot water the plastic may shrink and weaken the bottle.

Some people have tried to use chemical solvents to remove the glue residue on the

bottle. This might alter the walls of the bottle and make them too brittle or soft. Therefore

we don't recommend it.

#2 AFTER CLEANING

When launching, the pressure inside the bottle will cause the walls to expand. This

expansion leads to a loss of energy and will make the rocket fly to a lower altitude. To

solve this problem take some or duct tape, strapping tape, or packing tape and pre-wrap

three bands around the pressure chamber. You don't want the tape to be too bulky and

watch for wrinkles. This will strengthen the walls of the bottle without adding too much

mass and launch altitude will increase overall.

#3 NOSE CONES

Nose cones are not only for performance but add character and style to your rocket. Be sure to take

some time thinking out the design of your rocket before committing to a plan of action. Shown here is

only two examples; so don't be afraid to be creative.

My favorite is the "Bertha Series" nose cones, they are easy to make as well,

but require a little attention to detail. The "Bertha" nose cones are made by

cutting the bottom off a spare bottle with a pair of scissors and attaching the

top portion onto the pressure chamber. (Note: Never cut the pressure

chamber)  To mark a straight line around the bottle for cutting, I place the

bottle in a short can and hold a marker on the lip of the can as I rotate the

bottle. Before attaching the nose cone, add a small lump of Play-Doe or clay in

the bottle’s neck to increase the mass (see section on Rocket Concept). After

the Play-Doe is pushed in place tape over it with some duct tape and replace

the cap. Once you lance the rocket see how it hits the ground you will

understand the reason for the tape. Make sure you have a cap on the nose

cone. Before you tape the cone on, roll the rocket over a flat surface to make

sure the cone and pressure chamber align. A curvy rocket will not be safe

coming off the launcher.

This rocket is called "The Bullet". It is the easiest to make but lacks flight stability, this

can be fixed to a degree by pressing a small lump (a few ounces) of clay to the inside of

the nose cone. This will add mass to the cone and keep your rocket from flipping end

over end while in flight. The cone is made from poster board or tag board. You can

make the cone by simply cutting a large circle out of the poster board (about a 6 inch

radius). Cut a line from the outer edge of the circle to the center on the radius. Overlap

the cut edges and turn the circle while holding one edge stationary until you get the

desired cone shape. Secure the cone shape with staples or tape. Attach to the bottle

with tape or similar adhesive. (Note: do not puncture or cut the pressure chamber).

#4 FINS

Fins are the guidance system for your rocket. Without them a rocket would tumble end over end. Fins

can give your rocket life and beauty. Fins can portray aggressive power or aerodynamic grace.

However, fins tend to be the single greatest downfall of many young rocket builders. With the

incredible speeds and acceleration generated at launch, many fins get ripped off the rocket body

within a fraction of a second.

Fins should be firm; if they flop around they are useless.

Fins should be adequately secured; duct tape works well. I do not use glue because it does not

expand with the pressure chamber and may cause it to become brittle.

The best fins are made of rigid cardboard or styrofoam board.

The size of the fin does matter! The best rockets fly well with long and narrow fins.

Materials: (remember lightweight but sturdy)

Paper clips or Index Cards

Duct Tape or Clear packing tape

Cardboard (cheap, plentiful, soggy when wet)

Chipboard (cereal boxes)

Foam core (a little tougher but more $, some water damage)

Sturdi-board (like plastic cardboard, great stuff, $$, no water damage)

Balsa wood (might be a little heavy, fragile on impact)

Styrofoam sheets* (cheap, low mass, fragile on impact)

*Requires PL Premium Construction adhesive to attach

How many fins do I need?

To ensure stability and safety, the minimum number of fins on a rocket is three (3). Many people

choose a 3 or 4 fin design. There is no maximum number of fins you may have but keep in mind that

the more fins you have the more drag you will create and drag slows a rocket down.

Constructing fins

1. Be creative and cut out 3 or 4 identical fins. You can use any shape

except "forward swept" fins.

2. Lay the fin on a flat surface.

3. Use a paper clip bent at 90 degrees and taped it to the fin or an index

card taped onto the side of the fin. Be sure to leave a one-inch tab on the

index card. You will later bend this tab out 90 degrees to make an

attachable area for the rocket.

4. Repeat the same for the other side of the fin.

5. Repeat with other fins.

You should now have 3 or 4 fins each with either paper clips or two-index card tabs attached to the

fins. (If you use cardboard laminate the entire fin surface with tape to reduce the amount of water

damage to the fins.)

Fin placement

The fins of your rocket can't be placed above the halfway point of your pressure

cylinder. You want to place your fins at the base of the rocket to lower or maintain

the center of gravity. If you were to place the fins above the center of gravity, the

rocket would tumble and spin out of control once it left the launch pad.

Attaching the fins

This is the tricky part. Gluing the fins on is not recommended including hot glue and

"Liquid Nails" type adhesives are not flexible enough when it comes to the launch.

The bottle pressure chamber might expand a millimeter or more in circumference

when it is pressurized. That is enough to break the bonding seal of most glues.

When the rocket is launched, the fins usually rip off. I have found that tape works

the best at holding the fins on the rocket.

1. To find the location of the fins on the bottle, take a peace of string and wrap it

around the outside of the bottle and mark the length using an ink pen. Remove the

string from the bottle and lay it out in a straight line and mark the string in 3 or 4 equal lengths

depending on the number of fins you are going to use. Wrap the string around the bottle again and

transfer the marks to the bottle. If you are using 4 fins this will create 90-degree angles, 3 fins will be

at 120-degree angles. To mark a straight line on the bottle, lay it in a door jam and use the straight

edge to draw a line the length of your fin. You now have the locations of where to attach your fins.

2. Apply a piece of tape to the paper clip or index card tabs and carefully tape them to your rocket.

3. Look at your fin. Make sure it doesn't curve or it isn't crooked. It should be in a direct line with the

body of your rocket. If it isn't perfect, take it off and try again.

3. Attach the other fins. Test the wiggle of the fins. Your fins shouldn't wiggle more than a few

centimeters from side to side. Adding more tape to the top and bottom areas of the fin might fix this

problem.

Advance Design Water Bottle Rockets

The follow are some advance designs you can make with your rocket and require more work to build

but are fun to build.

PARACHUTE SYSTEMS

By now you may have spent about an hours building the rocket of your dreams. It may not be

completely obvious to you yet, but as the old saying goes, what goes up... must come down. It's time

to think about saving all that precious work by creating a recovery system for your rocket. Here are a

few ideas to get you started. Fins have been removed for clarity. (Note: you may substitute "crepe

paper streamers" for "parachute" in most of the following examples)

Here is a list of materials:

Tall kitchen garbage bag -or-   Kite string or Yarn

Four-grocery plastic bags    Baby Powder

Scotch Tape

The size and shape of your parachute can be as varied as your rocket. A good rule of thumb is to

make your chute 6 tot 12 inches across depending on a 1 or 2 liter bottle. Your chute could be larger

but some rocket styles have narrow nosecones and the chute could get stuck.

Making the Chute

Carefully cut the garbage bag along one side and the bottom seam. Open the bag along the fold and

lay it flat. If you want to use the grocery bags, cut each bag in the same way but lay them out side by

side 2 X 2. Use some scotch tape and tape the center seams to make a larger surface area.

The Square Chute

The simplest chute to make is the "Square Chute". Prepare the

edges, where you will connect the strings, with scotch tape

grommets. First apply a piece of tape to both sides of the plastic.

Then, with a hole punch, punch a clean hole through the center of the

tape and plastic tab. Repeat this procedure for each location where

you are placing a string.

To complete the "Square Chute", measure two 24-inch lengths of

string and tie each end to one of the grommet holes. Bring the

centers of the string loops together and tie them off.

The Circle Chute

The "Circle Chute" is a classic, timeless engineering masterpiece.

But don't let me influence you. If you have a large tire or similar

round object you can trace the circle on the plastic with a marker

and cut. If you don't have anything large enough to trace, fold the

plastic in half, then in half again, then fold on the diagonal. This will

give you a triangular wedge. With a sharp pair of scissors, cut along

the section that has the open edges. You don't have to worry about

cutting on the curve, just cut strait across the bottom. If you want to

practice this first, try cutting a piece of paper first. Finish the edges

with tape grommets as mentioned above. Lastly, tie separate 24 to

36 inch string leads to each grommet. Gather the leads together

and finish the strings off with a good knot.

Anti-Tangle Armature

One of the unforeseeable happenings in rocket parachuting is getting the strings

caught or tangled in the fins or safety lines of the rocket. An easy way to avoid this

problem is to build this simple cable shield for your chute. Cut two or three straws

into 4 or 6-inch sections. Slip the extra long string leads, from your parachute, into

the straw sections. The armature should protect the strings as the chute deploys

and then slide down out of the way when your chute opens up. (NOTE THE

ILLUSTRATION IS NOT TO SCALE.)

Folding the Chute

Dust the chute with baby powder to ensure that it doesn't stick to the side

of the rocket or itself. Grab the chute between two fingers, in the center,

and pull it up toward the ceiling. Let the chute fold naturally as you lift it.

Once you have the chute pulled up, fold it once in half at the center. You

don't want to fold the chute too tightly but you can fold your chute into

thirds if space is a factor. Wrap the excess string loosely around the chute.

Fold the straw armature sections onto the chute but not part of the excess

string wrap.

Making a Sleeve

If you find that the chute area is too small to hold your parachute, you

can increase the size of container by adding a section of chipboard

around the girth of the bottle. Or you can use another 2-liter bottle.

Remove the top and bottom of the 2nd 2-liter and tape the new cylinder

into position. This tends to make your rocket more stable by increasing

the distance between the Center of Pressure and the Center of Gravity.

The "Bertha Cone Chute" (3 out of 5 Stars)

With this chute system, instead of taping the nose cone on, attach a safety

cord to the weighted cone and apply a parachute to the top of the pressure

cylinder. In theory, once the rocket reaches apogee (the highest point of

travel), the weighted nose cone separates from the main body. The main body

is creating enough drag to slow itself down. If everything works, the parachute

deploys and the two pieces float gently back down to earth.

In practice, the nose cone can sometimes get jammed on the main body

causing a failure. In addition, safety cord can be too short and the cone can't

clear the body.

Nose Cone Tug Chute (3 out of 5 Stars)

The "Tug Chute" uses the force of the lifting nose cone to pull the chute out

of the sleeve or needle assembly. Attach a safety line to the nose cone

or tennis ball. Attach a parachute close to the cone/ball assembly. The

chute needs to be folded small enough to fit inside the needle yet not too tight

to unravel.

Problems with this system include; not enough line and parachute packing

jams. Cone style noses with a sleeve have more success with this system.

The "Space Needle" style of nose cone can be made from a spare bottle, empty paper

towel roll, and a tennis ball or racket ball. This type of nose cone adds a great deal of

inertial mass to the rocket and makes it really stable. Simply, attach the towel roll to the

top of a single Bertha nose cone and then fix the tennis ball to the top of the roll. Take

your time building this set up because you want the entire assembly to be straight as an

arrow.

Cut tabs in an index card and glue or tape the card to the tube. This will hold

the tube upright. Then tape the tabs onto the nose cone top.